## Slide 1
1

## Slide 2: Memory Compiler
Ashish Shukla
21st Oct, 2021
Acknowledgement: Mingoo Seok, previous TAs, Columbia

## Slide 3: Memory Compiler
Use of Standard Library 130nm to 250nm SRAM generators to create instances with a variety of parameters and views
One can generate single and dual-port, high speed and high density SRAM.
Located at:
/courses/ee6321/share/mem_comp

## Slide 4: SRAM Generator Features
Optimized for High Speed/Density or Low-Power or High Density
Aspect Ratio Control for Efficient Floor Planning
Memory Operation and Retention at Low Frequency
Low Active Power and Leakage-Only Standby Power
Timing and Power Models for Industry-Leading Design Tools
Configurable Word-Write Mask Option

## Slide 5: Generating SRAM example (1)
Create “mem_comp” folder in your directory
Copy the contents from
/courses/ee6321/share/mem_comp to your local folder
Use For one-port memory “/courses/ee6321/share/mem_comp/rf1shd/bin/rf1shd” For two-port memory “/courses/ee6321/share/mem_comp/ra2shd_v20/bin/ra2shd_v20”

## Slide 6: SRAM Standard Support
PostScript Datasheet
ASCII Datatable
Verilog Model ( .v)
VHDL Model
Synopsys Model ( .lib)
PrimeTime Model ( .data .mod)
TLF Model
VCLEF Footprint
GDSII Layout
LVS Netlist

## Slide 7: Generating SRAM example (2)
Memory Parameters
Choose output file listed in slide 4
! There is a limited range for each parameters
Number of Words
- [16, 256]
Number of Bits - [4, 128]
Notes: Explain the parameters in detail

## Slide 8: Generating SRAM example (3)
OR Under “Generate Menu” to generate files needed in one shot

## Slide 9: Outputs You Need
Please use 1.2V 25℃ as your library file for assignment 4, you can try different libraries later if you want
Instantiation name
.v can be used in Modelsim simulation
Notes: rf1shd/bin/rf1shd

## Slide 10: Sram Ports

## Slide 11: Detailed function description
All the details of the sram will be in ra2shd_v20.pdf (Artisan User Manual)
Design & memory-compiler.pdf is slides for memory compiler from ARES Lab

## Slide 12: Sram Read Timing Diagram
Data (Q) will be available after the rising edge of the clock (1 clock cycle delay)

## Slide 13: Sram Write Timing Diagram

## Slide 14: Summary
Behavioral Verilog
*.v
testbench tb*.v
functional
verification
post-synthesis dynamic timing verification
Structural Verilog
*.nl.v
std. cell lib
*.db *.sldb
constraints
*.sdc
Design Compiler
ModelSim
Timing info.
*.sdf
ModelSim
static timing verification
PrimeTime
power analysis
Encounter
Automatic Placement and Routing
Memory Compiler (*.v, *.lib, & *.vclef)
Memory Compiler

## Slide 15: Suggestions on Lab Assignment 4
Make sure you are familiar with previous labs
Take a look at the Memory Generator User Manual to learn the architecture & timing specification of SRAM.
First simulate the sram block you generated from memory compiler and then try to build the larger block. (RTL on-chip memory model guide.pdf as reference).
When running DC, you do not need to use read_verilog to include the [mem_cell_name].v generated by memory compiler and you do not need to use command to black-box your sram. You only need to include the correct db file. (.db file is generated by compiling .lib file through DC, codes are in /courses/ee6321/share/4823-fall2020/lib2db/).
You can use the same db file as above in your PT
Start early. This one will take some time.